## Slide 1
FINAL PROJECT REVIEW
ForearmSense AI
EMG and motion-based grip activity
and stability analysis
AECD · 25EC1302E
KL University, Hyderabad
A Jaswant Goud 2510040007 G Abhishek 2510040015
O GopiChand 2510040023 C Meghasyam 2510040072
Notes: Sources: README.md and project.json. Current deliverable is a synthetic laboratory. The available-hardware design uses Uno, one BioAmp EXG Pill, MPU-6050 and a hand gripper.

## Slide 2
Problem and project objectives
ForearmSense AI
02
Muscle activity needs
movement context
EMG describes electrical activation. Motion sensing distinguishes a steady grip from a grip with movement.
Activity analysis
Activation timing and repetition consistency
Movement stability
Acceleration and angular rate
Concept illustration, not the built prototype
Notes: Project sources: docs/ForearmSense_AI_AECD_PBL_REVISED_UNO.md, sections 1.1–1.5
Illustration: built-in image generation. Prompt: scientific editorial forearm and hand squeezing a spring gripper, three surface electrodes, white and mint background, forest green accents, no text or clinical claims. Concept only, no validated electrode placement or wiring.

## Slide 3
Available hardware and its role
ForearmSense AI
03
Component | Role | Measurement boundary
BioAmp EXG Pill | One analog EMG channel | Gain and filtering unverified
Arduino Uno | ADC and serial transport | Revision and rate unverified
MPU-6050 | Acceleration and gyro | Ranges and mounting unverified
Hand gripper | Repeatable grip/release task | No force measurement
Confirmed inventory. Live acquisition and calibration remain planned.
Notes: Project sources: project.json; docs/fixed-hardware-project-map.md

## Slide 4
Planned hardware data path
ForearmSense AI
04
Forearm
electrodes
BioAmp
EXG Pill
Arduino Uno
ADC + serial
Laptop
FastAPI + React
MPU-6050
Accel + gyro
Analog EMG
Motion data
The gripper provides the task. It does not measure force.
Functional design only. Verify the board, firmware, sampling and calibration before live use.
Notes: Sources: project.json; docs/fixed-hardware-project-map.md. Functional diagram only. Live serial ingestion and calibration remain planned. No pin-level wiring or electrode placement is prescribed.

## Slide 5
Software workflow
ForearmSense AI
05
Generate
a seeded trial
Model analog
conditioning
Extract EMG
and IMU features
Review results
and export
Saved synthetic signal example
FastAPI backend + React/TypeScript frontend
Notes: Project sources: README.md; docs/architecture.md; docs/dsp-pipeline.md

## Slide 6
Analog conditioning and digital processing
ForearmSense AI
06
High-pass
20 Hz
Notch
50 Hz, optional
Low-pass
450 Hz
ADC model
12-bit, 4 kHz
Educational filter model
Digital analysis
200 ms windows
100 ms hop
RMS and spectral features
FIR output at 1 kHz
A 250 Hz raw stream cannot preserve a 450 Hz EMG band.
Notes: Project sources: docs/dsp-pipeline.md; docs/analog-design.md; results/metrics/trial-seed42.json
Image source: results/figures/frequency-analysis.png, magnitude panel. This chain is educational and does not describe verified BioAmp hardware settings. FIR output guarantees a passband through 400 Hz.

## Slide 7
Interactive simulation dashboard
ForearmSense AI
07
Adjust scenarios, inspect waveforms and export the full numerical trial.
Saved simulation view. Navigation predates report alignment.
Notes: Project sources: results/figures/dashboard-desktop.png, historical saved screenshot; README.md

## Slide 8
Saved signal analysis results
ForearmSense AI
08
Seed 42 · 2 seconds · 4 kHz · 8,000 samples
Chart: Time (s)
| 0.00 | 0.05 | 0.10 | 0.15 | 0.20 | 0.25 | 0.30 | 0.35 | 0.40 | 0.45 | 0.50 | 0.55 | 0.60 | 0.65 | 0.70 | 0.75 | 0.80 | 0.85 | 0.90 | 0.95 | 1.00 | 1.05 | 1.10 | 1.15 | 1.20 | 1.25 | 1.30 | 1.35 | 1.40 | 1.45 | 1.50 | 1.55 | 1.60 | 1.65 | 1.70 | 1.75 | 1.80 | 1.85 | 1.90 | 1.95
50 ms RMS (mV) | 0.1772 | 0.15732 | 0.13181 | 0.12138 | 0.12594 | 0.14811 | 0.16924 | 0.20324 | 0.23373 | 0.25727 | 0.34908 | 0.38864 | 0.39586 | 0.30062 | 0.3437 | 0.2682 | 0.25675 | 0.21384 | 0.14844 | 0.14052 | 0.090471 | 0.080961 | 0.079281 | 0.081215 | 0.080119 | 0.068197 | 0.084122 | 0.080306 | 0.092576 | 0.10256 | 0.11427 | 0.14752 | 0.23611 | 0.20611 | 0.319 | 0.31734 | 0.38124 | 0.33909 | 0.30618 | 0.32621
0.226 mV
Whole-trial RMS
211.7 Hz
Mean frequency
0 modeled clipping events
Synthetic ADC-derived signal, referred to the model input. No physiological measurement.
Notes: Project sources: results/metrics/summary.json; results/metrics/trial-seed42.json

## Slide 9
Machine learning evaluation workflow
ForearmSense AI
09
30 synthetic trials
5 gesture classes
200 ms windows
50% overlap
570 windows
EMG + IMU features
Three folds hold out complete trials
Training trials
Fit feature scaling + model
Held-out trials
Predict once per window
Logistic Regression, SVM, Decision Tree, Random Forest, Gradient Boosting
Windows from the same trial never appear in both training and test data.
Notes: Sources: docs/ml-methodology.md; results/ml/metrics.json. Three outer folds group windows by trial. StandardScaler stays inside training pipelines. SVM has nested grouped probability calibration. Five models and three modality comparisons.

## Slide 10
Synthetic machine learning benchmark
ForearmSense AI
10
Chart: 
| EMG only | IMU only | EMG + IMU
Random Forest OOF accuracy | 0.35088 | 0.98947 | 0.90526
Random Forest comparison
30 trials
570 windows
5 gesture classes
3-fold trial-grouped evaluation keeps overlapping windows from the same trial together.
IMU outperforms fusion here. Programmed movement patterns limit generalization.
Synthetic results only. No independent model-selection holdout or human validation.
Notes: Project sources: results/ml/metrics.json; results/ml/benchmark-report.md; docs/ml-methodology.md

## Slide 11
Engineering and software verification
ForearmSense AI
11
SPICE: partial
Ideal R/C response agrees
within 1.45 x 10^-7 dB.
OPA2376 gain check passed.
INA826 gain check failed.
Recorded software checks
62 backend tests passed
Build and ESLint passed
7 browser cases across two runs
Component tolerance study
Saved analytical study. No physical hardware validation.
Notes: Project sources: results/spice/verification.json; docs/verification.md, report alignment record 2026-10-23
Image: results/figures/component-tolerances.png. Candidate Sallen-Key model, ideal buffers, R +/-1%, C +/-5%, notch omitted. Simulation ranges are not guarantees for physical modules.

## Slide 12
Planned 35-second grip protocol
ForearmSense AI
12
Three 5-second squeezes separated by rest
Rest
0-5 s
Squeeze
5-10 s
Rest
10-15 s
Squeeze
15-20 s
Rest
20-25 s
Squeeze
25-30 s
Rest
30-35 s
Rest phases
Baseline and relaxation
Squeeze phases
Activation timing, envelope consistency
and movement steadiness
Notes: Project sources: project.json task_protocol; docs/ForearmSense_AI_AECD_PBL_REVISED_UNO.md

## Slide 13
Current completion and remaining work
ForearmSense AI
13
Implemented | Next implementation phase
Synthetic EMG and motion generation | Verify firmware, ADC and actual sample timing
Analog/DSP analysis and JSON export | Validated serial ingestion with disconnect handling
Grouped ML training and prediction | Baseline calibration and 35-second acquisition
Engineering checks and local dashboard | Raw recording, replay and real-data evaluation
Unavailable measurements: grip force, SpO₂ and blood flow. No clinical claims.
Notes: Project sources: project.json; docs/report-alignment.md; README.md

## Slide 14
Conclusion and next milestone
ForearmSense AI
14
A reproducible laboratory for
EMG and movement analysis
The project connects analog signal conditioning, digital analysis and grouped ML evaluation in one local application.
Next milestone
Verify the Uno/BioAmp/MPU-6050 stream, then complete one calibrated, recorded grip session.
Notes: Project sources: README.md; project.json; revised report conclusion